## Slide 1: Computer Architecture Seminar/Proseminar Lecture 1b: Example Presentation
A. Giray Yaglikci
27 April 2026

## Slide 2: BreakHammer: Enhancing RowHammer Mitigations by Carefully Throttling Suspect Threads
Oğuzhan Canpolat A. Giray Yağlıkçı Ataberk Olgun İsmail E. Yüksel
Yahya C. Tuğrul Konstantinos Kanellopoulos Oğuz Ergin Onur Mutlu
Venue : MICRO 2024
Presenter : A. Giray Yaglikci
Date : 27 April 2026
Notes: Hi all. I am Oğuzhan, very excited to be here and be able to present our work BreakHammer: Enhancing RowHammer Mitigations by Carefully Throttling Suspect Threads.

## Slide 3: Executive Summary
Goal: Reduce the performance overhead of RowHammer mitigation mechanisms by reducing the number of performed RowHammer-preventive actions without compromising system robustness
Problem:
DRAM continues to become more vulnerable to RowHammer
RowHammer-preventive actions are time consuming and block access to memory
Key Results: BreakHammer significantly reduces the negative effects of RowHammer mitigation mechanisms on performance, energy, and fairness
Key Idea: Throttle threads that frequently trigger RowHammer solutions
Key Mechanism: BreakHammer
Observes triggered RowHammer-preventive actions
Identifies threads that trigger many preventive actions (i.e., suspect threads)
Reduces the memory bandwidth usage of the suspect threads
https://github.com/CMU-SAFARI/BreakHammer
Key Exploit: Mount a memory performance attack by triggering
RowHammer-preventive actions to block memory access for long time periods
Notes: Here is an executive summary of my talk:
[CLICK] DRAM continues to become more vulnerable to RowHammer…
Operations that prevent RowHammer, which we call…
[CLICK] We introduce a new exploit where one can mount a memory performance attack…
[CLICK] Our goal is to…
[CLICK] Our key idea is to throttle threads…
[CLICK] To this end, we propose a new mechanism, BreakHammer: which
[CLICK] Observes triggered RowHammer-preventive actions
[CLICK] Identifies threads that trigger many preventive actions (we call such threads suspect threads), and
[CLICK] Reduces the memory bandwidth usage of the suspect threads
[CLICK] Our rigorous evalutions show that BreakHammer significantly reduces the negative effects of RowHammer solutions on performance, energy, and fairness
[CLICK] BreakHammer and all of our datasets are fully open-sourced and available online
====
Don’t say unfairness

## Slide 4: Taking a Step Back: What is an Executive Summary?
Summary of the paper in a nutshell
Tells what this paper/talk about and sets expectations
Serves the same purpose as the paper’s abstract
Helps the reader/audience to decide if they want to
  read the rest of the paper
  pay attention to the rest of the talk

## Slide 5: Outline
Background
Conclusion
BreakHammer
Evaluation
Motivation
Notes: Here is the outline of my talk, I’ll continue with a brief background on DRAM and DRAM read disturbance

## Slide 6: DRAM Organization
DRAM
Channel
DRAM Module
DRAM Chips
Notes: Here I show a typical computing system with a processor and a DRAM module connected through the DRAM channel
[CLICK] A DRAM module contains multiple DRAM chips

## Slide 7: DRAM Organization
Bitline
S
S
S
S
Sense Amplifiers
(Row Buffer)
Wordline
DRAM Cell
Bank
DRAM Array
Off-Chip Channel
Notes: and a DRAM chip [CLICK] contains several DRAM banks
[CLICK] inside each DRAM bank, we have a two dimensional array of DRAM cells
[CLICK] where a DRAM cell stores a single bit of information as electrical charge
[CLICK] DRAM cells are horizontally organized as DRAM rows and are connected via wordlines
[CLICK] and they are vertically connected to sense amplifiers via bitlines for DRAM accesses

## Slide 8: RowHammer: A Prime Example of Read Disturbance
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
DRAM Subarray
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes read disturbance bitflips in nearby cells
Notes: DRAM is accessed at a row granularity, however today, this access is not perfect
Where it is vulnerable to read disturbance, here I show a prime example of DRAM read disturbance, called RowHammer
Where repeatedly [CLICKx4] opening and closing a DRAM row induces bitflips in nearby unaccessed DRAM cells
[CLICK] in RowHammer terminology, we refer the repeatedly opened row as the aggressor row
and we refer the nearby unaccessed rows that experience bitflips as the victim rows
======
repeatedly?

## Slide 9: Read Disturbance Vulnerabilities (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
DRAM Subarray
The minimum number of activations that causes a bitflip is called the RowHammer threshold (NRH)
Notes: We denote the minimum amount of activations to cause a bitflip as the RowHammer threshold, or NRH

## Slide 10: Read Disturbance Vulnerabilities (II)
Technology Scaling
It is critical to prevent read disturbance bitflips
effectively and efficiently for highly vulnerable systems
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
Notes: DRAM modules are continuously becoming more vulnerable to read disturbance over generations
[CLICK] over the last decade, we have seen more than two orders of magnitude decrease in the necessary activations to induce the first bitflip
[CLICK] therefore, it is critical to effectively and efficiently prevent these bitflips

## Slide 11: Read Disturbance Vulnerabilities (II)
Technology Scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
It is critical to prevent read disturbance bitflips
effectively and efficiently for highly vulnerable systems
This is a takeaway box, use it
Explicitly tells the audience
your take from the slide and what they should remember
Notes: DRAM modules are continuously becoming more vulnerable to read disturbance over generations
[CLICK] over the last decade, we have seen more than two orders of magnitude decrease in the necessary activations to induce the first bitflip
[CLICK] therefore, it is critical to effectively and efficiently prevent these bitflips

## Slide 12: RowHammer-Preventive Actions
Many ways to prevent RowHammer via RowHammer-preventive actions:
Preventive refresh
Row migration
Proactive throttling
…
State-of-the-art RowHammer mitigations adopt these two approaches
Notes: There are many ways proposed to prevent RowHammer with what we call RowHammer-preventive actions
[CLICK] Here I show a non exhaustive list of actions one can perform to mitigate RowHammer bitflips
[CLICK] In our talk, we will focus on these preventive refresh and row migration, as state-of-the-art solutions adopt these RowHammer-preventive actions
=====
Name them here

## Slide 13: Preventive Refresh as a RowHammer-Preventive Action
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM
Refreshing potential victim rows mitigates RowHammer bitflips
Aggressor Row
Notes: One of these ways is to [CLICK] preventively refresh the potential victims of an aggressor row before they experience bitflips

## Slide 14: Row Migration as a RowHammer-Preventive Action
Row 0
Row 1
Row 2
Row 4
Row 2
open
Row 1
Row 2
closed
Row 2
open
Row 1
Row 0
Distant Row
Victim Row
Aggressor Row
Aggressor Row
Row 2
open
Row 2
DRAM
Migrating potential aggressor rows
to a distant row mitigates RowHammer bitflips
Victim Row
Aggressor Row
…
Notes: And another way is to [CLICK] move the contents of an aggressor row to a distant row away from its potential victims
before it has been activated enough times to induce a bitflip

## Slide 15: Outline
Background
Conclusion
BreakHammer
Evaluation
Motivation
Notes: I’ll continue with the motivation of our work

## Slide 16: Root Cause of Performance Overhead
REF
DRAM
Channel
DRAM Module
RowHammer-preventive actions are blocking and time consuming operations
ACT
Memory controller cannot access a memory bank
undergoing a RowHammer-preventive action
Refreshing KBs of data can block access to GBs of data
Notes: One of the problem with RowHammer-preventive actions is that they are blocking operations
[CLICK] where the memory controller cannot access a memory bank undergoing a RowHammer-preventive action
[CLICK] As such, refreshing KBs of data can block access to GBs of data

## Slide 17: RowHammer Mitigation Performance Overhead
Lower is worse
Lower is worse
Preventive Refresh
Row Migration
Notes: We analyze the system performance impact of blocking RowHammer-preventive actions by evaluating four state-of-the-art RowHammer solutions
[CLICK] Here, the X axis shows the decreasing RowHammer threshold
[CLICK] the Y axis shows the weighted speedup, normalized to a system with no RowHammer defense
[CLICK] and each bar identifies a different RowHammer mitigation mechanism
Hydra, RFM, and PARA use preventive refresh
And AQUA uses row migrations
[CLICK] From our analysis, we observe that RowHammer mitigation mechanisms incur significantly increasing performance overhead as the RowHammer threshold decreases

## Slide 18: RowHammer Mitigation Performance Overhead
RowHammer mitigation mechanisms incur increasingly large performance overhead as the RowHammer threshold decreases
19%
66%
Preventive Refresh
Row Migration
Notes: We analyze the system performance impact of blocking RowHammer-preventive actions by evaluating four state-of-the-art RowHammer solutions
[CLICK] Here, the X axis shows the decreasing RowHammer threshold
[CLICK] the Y axis shows the weighted speedup, normalized to a system with no RowHammer defense
[CLICK] and each bar identifies a different RowHammer mitigation mechanism
Hydra, RFM, and PARA use preventive refresh
And AQUA uses row migrations
[CLICK] From our analysis, we observe that RowHammer mitigation mechanisms incur significantly increasing performance overhead as the RowHammer threshold decreases

## Slide 19: Presenting a Plot
Explain the plot before making observations
  What do the axes show?
  Which way is better?
  What are the colors?
Highlight observations
Give your key takeaway
RowHammer mitigation mechanisms incur increasingly large performance overhead as the RowHammer threshold decreases
19%
66%
Preventive Refresh
Row Migration
Transparent boxes are your friends
Notes: We analyze the system performance impact of blocking RowHammer-preventive actions by evaluating four state-of-the-art RowHammer solutions
[CLICK] Here, the X axis shows the decreasing RowHammer threshold
[CLICK] the Y axis shows the weighted speedup, normalized to a system with no RowHammer defense
[CLICK] and each bar identifies a different RowHammer mitigation mechanism
Hydra, RFM, and PARA use preventive refresh
And AQUA uses row migrations
[CLICK] From our analysis, we observe that RowHammer mitigation mechanisms incur significantly increasing performance overhead as the RowHammer threshold decreases

## Slide 20: Memory Performance Attack
Attacker can trigger many preventive actions
to block access to main memory
Preventive actions can be exploited
to reduce DRAM bandwidth availability
Memory
Controller
Core
Core
Attacker
User
Notes: Even worse, at these lower thresholds, RowHammer-preventive actions become a potential memory performance attack vector
[CLICK] where an attacker can intentionally trigger many of RowHammer-preventive actions
and cause a DRAM module to get blocked for extended periods of time, thereby reducing DRAM bandwidth availability
=====
Use whitespace, separate attacker and user
Maybe change the user icon
Use a sad icon

## Slide 21: Problem & Goal
Operations that prevent RowHammer lead to
DRAM bandwidth availability issues
as they can frequently block access to memory
Problem
Reduce the performance overhead of RowHammer mitigation mechanisms by reducing the number of RowHammer-preventive actions
without compromising system robustness
Goal
Notes: Therefore, the problem we tackle is [STOP] operations that prevent RowHammer become a system performance vulnerability as they can frequently block access to memory
[CLICK] and our goal is to reduce the performance overhead of RowHammer mitigation mechanisms by reducing the number of performed RowHammer-preventive actions without compromising system robustness

## Slide 22: Outline
Background
Conclusion
BreakHammer
Evaluation
Motivation
Notes: To this end, we propose a new mechanism, BreakHammer

## Slide 23: Key Idea
Memory
Controller
Core
Core
Attacker
User
Detect and slow down the memory accesses of threads
that trigger many RowHammer-preventive actions
Suspect Thread
Notes: BreakHammer’s key idea is to detect and slow down the memory accesses of threads that trigger many RowHammer-preventive actions
[CLICK] We refer to these threads as suspect threads

## Slide 24: BreakHammer: Overview
Execution Timeline
Throttling Window
Throttling Window
Throttling Window
Time
T3
T4
T4
T2
T4
T1
Thread 1’s Row Activations
REFP
RowHammer-Preventive Action
T1
REFP
Thread
Score
T1
T2
T3
T4
10 ↑↑
2 ↑
3 ↑
50 ↑↑↑
Observing RowHammer-
Preventive Actions
T1
T2
T3
T4
Suspect
Identifying Suspect Threads
LD
LD
LD
LD
Throttling Memory
Bandwidth Usage
1
2
3
Notes: Here I show a cartoonish execution overview of BreakHammer.
[CLICK] BreakHammer divides the execution timeline into periods of equal length which we call Throttling Windows
[CLICK] and views the execution as a stream of row activations from different threads, and RowHammer-preventive actions
Whenever a RowHammer-preventive action is triggered, BreakHammer performs three key operations:
[CLICK] First, BreakHammer attributes what we call a RowHammer-preventive score to each thread proportional to their contribution to the given RowHammer-preventive action
[CLICK] Next, BreakHammer performs outlier analysis on the attributed scores
And detects suspect threads that unfairly reduce DRAM bandwidth availability
[CLICK] Lastly, BreakHammer slows down suspect threads by reducing their memory bandwidth usage
====
Try to say the section titles as well

## Slide 25: BreakHammer: Overview
Execution Timeline
Throttling Window
Throttling Window
Throttling Window
Time
T3
T4
T4
T2
T4
T1
Thread 1’s Row Activations
REFP
RowHammer-Preventive Action
T1
REFP
Thread
Score
T1
T2
T3
T4
10 ↑↑
2 ↑
3 ↑
50 ↑↑↑
Observing RowHammer-
Preventive Actions
T1
T2
T3
T4
Suspect
Identifying Suspect Threads
LD
LD
LD
LD
Throttling Memory
Bandwidth Usage
1
2
3
Notes: Now let’s take a deeper look on how BreakHammer attributes RowHammer-preventive scores
=====
Subscript p for REFs, they are not periodic refreshes

## Slide 26: Observing RowHammer-Preventive Actions
BreakHammer tracks the number
of RowHammer-preventive actions each thread triggers
Thread 1
Thread 2
Thread 3
Thread 4
RowHammer-preventive score counter
Notes: BreakHammer tracks the number of RowHammer-preventive actions each hardware thread triggers
[CLICK] To do so, BreakHammer implements a counter called RowHammer-preventive score for each hardware thread

## Slide 27: Score Attribution Method
Time
A RowHammer-preventive action is generally caused by
a stream of memory requests from many hardware threads
Thread 1
Thread 2
Thread 3
Thread 4
T2
T3
T4
T4
T1
T4
T4
T1
Thread 1’s Row Activations
REFP
RowHammer-Preventive Action
RH-Preventive Score
Notes: The challenge with updating scores is that
one cannot directly attribute a RowHammer-preventive action to a single thread
because a RowHammer-preventive action is generally caused by a stream of memory requests contributed by many hardware threads
[CLICK] Here on the bottom I show a timeline of DRAM row activations and RowHammer-preventive actions
[CLICK] Where a stream of row activations from multiple threads trigger a preventive action
[CLICK] When a preventive action is triggered, BreakHammer attributes a score to each thread
PROPORTIONAL to the number of row activations the thread performed for the observed action

## Slide 28: Integration Showcase
1)
Probabilistic Row Activation (PARA)
2)
Per Row Activation Counting (PRAC)
Notes: BreakHammer cooperates with existing RowHammer solutions
Therefore, observed RowHammer-preventive actions change depending on the mechanism BreakHammer is integrated with
Here I show two examples on how BreakHammer can be integrated with existing solutions
====
Do not be Turkish on PARA

## Slide 29: Integration Showcase
1)
Probabilistic Row Activation (PARA)
2)
Per Row Activation Counting (PRAC)
Notes: BreakHammer cooperates with existing RowHammer solutions
Therefore, observed RowHammer-preventive actions change depending on the mechanism BreakHammer is integrated with
Here I show two examples on how BreakHammer can be integrated with existing solutions
====
Do not be Turkish on PARA

## Slide 30: Integration Showcase with PARA (I)
BreakHammer cooperates with existing RowHammer solutions
Probabilistic Row Activation (PARA) [Kim+, ISCA 2024]:
  Generates a random number
  Compares the number with a threshold
  If the random number exceeds the threshold performs a preventive refresh
access
refreshP
>?
Notes: In systems protected with PARA, whenever a DRAM row is activated
[CLICK] PARA generates a random number and compares it with a threshold
[CLICK] if the random number exceeds the threshold, PARA performs a preventive refresh

## Slide 31: Integration Showcase with PARA (II)
Probabilistic Row Activation + BreakHammer (PARA+BH):
  Track row activation count of each thread between preventive refreshes
  Increment each thread’s score proportionally to its activations
access
T2
T3
T3
T1
T3
T1
T3
refreshP
Time
Thread 1
Thread 2
Thread 3
refreshP
RH-Preventive Score
Notes: When we integrate BreakHammer with PARA:
[CLICK] BreakHammer tracks the row activation count of each thread between preventive refreshes
[CLICK] And whenever a preventive refresh is performed, increments each thread’s score proportionally to its activation count

## Slide 32: Integration Showcase
1)
Probabilistic Row Activation (PARA)
2)
Per Row Activation Counting (PRAC)
Notes: BreakHammer cooperates with existing RowHammer solutions
Therefore, observed RowHammer-preventive actions change depending on the mechanism BreakHammer is integrated with
Here I show two examples on how BreakHammer can be integrated with existing solutions
====
Do not be Turkish on PARA

## Slide 33: Integration Showcase with PRAC (I)
BreakHammer cooperates with existing RowHammer solutions
Per Row Activation Counting (PRAC) [JEDEC, 2024]:
  DRAM maintains an activation counter for each DRAM row
  DRAM requests time by triggering a back-off
  Memory controller provides time for in-DRAM preventive refreshes
Counter 0
Counter 1
...
Counter 3
Per Row
Activation Counters
back-off
RFM
High Activation
Count Detected
Notes: With PRAC
[CLICK] DRAM maintains an activation counter for each DRAM row
[CLICK] Whenever one of these counters reaches a critical value
For example close to RowHammer threshold
[CLICK] The DRAM module triggers whats called a back-off
[CLICK] After a back-off is received by the memory controller
It stops performing accesses to DRAM
And starts sending special commands that allow time for preventive refreshes
=====
Make the arrow shorter for high activation count
Refreshes should be refresh with subscript ps

## Slide 34: Integration Showcase with PRAC (II)
Per Row Activation Counting + BreakHammer (PRAC+BH):
  Track row activation count of each thread between back-offs
  Increment each thread’s score proportionally to its activations
back-off
access
T2
T3
T3
T1
T3
T1
T3
back-off
Time
Thread 1
Thread 2
Thread 3
RH-Preventive Score
Notes: When we integrate BreakHammer with PRAC:
[CLICK] BreakHammer tracks the row activation count of each thread between back-offs
[CLICK] And when a back-off is observed, BreakHammer increments each thread’s score proportionally to its activation count

## Slide 35: Integration with Other Mechanisms
We integrate BreakHammer with eight RowHammer solutions:
https://github.com/CMU-SAFARI/BreakHammer
https://arxiv.org/abs/2404.13477
PARA [Kim+, ISCA 2014]
Graphene [Park+, MICRO 2020]
Hydra [Qureshi+, ISCA 2022]
TWiCe [Lee+, ISCA 2019]
AQUA [Saxena+, MICRO 2022]
REGA [Marazzi+, S&P 2023]
RFM [JEDEC 2020]
PRAC [JEDEC 2024]
Notes: BreakHammer is compatible with many types of RowHammer solutions including both in-memory controller and in-DRAM RowHammer mitigation mechanisms as we have seen.
In our paper, we integrate BreakHammer with eight state-of-the-art RowHammer solutions.
I would like to refer you to our paper or open-source repository for their integration.

## Slide 36: BreakHammer: Overview
Execution Timeline
Throttling Window
Throttling Window
Throttling Window
Time
T3
T4
T4
T2
T4
T1
Thread 1’s Row Activations
REFP
RowHammer-Preventive Action
T1
REFP
Thread
Score
T1
T2
T3
T4
10 ↑↑
2 ↑
3 ↑
50 ↑↑↑
Observing RowHammer-
Preventive Actions
T1
T2
T3
T4
Suspect
Identifying Suspect Threads
LD
LD
LD
LD
Throttling Memory
Bandwidth Usage
1
2
3
Notes: Let’s continue by looking at how BreakHammer identifies suspect threads

## Slide 37: Identifying Suspect Threads: An Example
BreakHammer detects threads that trigger too many RowHammer-preventive actions
>
Minimum Score
to Consider
Maximum Deviation
from the Average Score
Threads
Score
Thread
Score
T1
10
T2
2
T3
3
T4
50
…
…
Notes: BreakHammer identifies suspect threads by detecting threads that trigger too many RowHammer-preventive actions
Here on the left, we have the RowHammer-preventive scores of threads in the system
[CLICK] We can visualize these scores as a distribution
Where the bars show different threads
And the height of the bars show the score of each thread
BreakHammer detects a suspect with two checks
[CLICK] First, BreakHammer checks if a thread’s score exceeds a minimum score to consider
This allows BreakHammer to protect threads with low memory intensity against suspect detection
[CLICK] Second, BreakHammer checks if a thread’s score largely exceeds the average score of all hardware threads
Doing so allows BreakHammer to detect suspect threads that unfairly reduce DRAM bandwidth availability
=====
Maximum deviation is not coming out
Do not waste white space
Add text about average score
Do not keep stuff close to each other use white space

## Slide 38: BreakHammer: Overview
Execution Timeline
Throttling Window
Throttling Window
Throttling Window
Time
T3
T4
T4
T2
T4
T1
Thread 1’s Row Activations
REFP
RowHammer-Preventive Action
T1
REFP
Thread
Score
T1
T2
T3
T4
10 ↑↑
2 ↑
3 ↑
50 ↑↑↑
Observing RowHammer-
Preventive Actions
T1
T2
T3
T4
Suspect
Identifying Suspect Threads
LD
LD
LD
LD
Throttling Memory
Bandwidth Usage
1
2
3
Notes: Lastly, let’s understand how BreakHammer throttles a suspect thread

## Slide 39: Throttling Memory Bandwidth Usage of Suspect Threads
BreakHammer reduces the memory bandwidth usage
of each suspect thread
Throttle
BreakHammer
Last-Level Cache
Cache-Miss Buffers*
Allocated
Maximum
0
∞
0
∞
0
∞
0
∞
3
∞
1
∞
2
∞
4
∞
5
5
5
User
User
User
Suspect
Notes: BreakHammer reduces the memory bandwidth usage of each suspect thread
There are many ways to reduce the memory bandwidth usage
[CLICK] For our implementation, we chose to limit the allocatable cache-miss buffers
Which track the requests that miss the last-level cache and are being served by the memory controller
[CLICK] At system boot, all threads have 0 allocated cache-miss buffers
and they are allowed to allocate all available cache-miss buffers in the system
[CLICK] As the threads execute and access main memory, they start allocating cache-miss buffers
[CLICK] When BreakHammer identifies a thread as suspect
It limits the number of cache-miss buffers the thread can allocate in the last-level cache
[CLICK] If a thread reaches their allocation limit
[CLICK] they can no longer make new request to main memory and must wait for their earlier requests to be resolved

## Slide 40: Restoring Memory Bandwidth of Suspect Threads
BreakHammer restores the memory bandwidth usage of a suspect thread if the thread stays benign for the full duration of a throttling window
Execution Timeline
Throttling Window
Benign
Throttling Window
Throttled
Suspect
Identified
This Window
Memory Bandwidth
Usage Restored
Still
Throttled
Throttling Window
Benign
Not
Identified
Notes: BreakHammer restores the memory bandwidth usage of a suspect thread back
If the thread stays benign for the full duration of a throttling window
Here on the bottom I show a execution timeline for an example
[CLICK] In the example, our thread is identified as a suspect in the first window, where BreakHammer immediately throttles their memory bandwidth usage
[CLICK] On the second window, the thread continues to execute with a reduced memory bandwidth
Where the thread stays benign and does not get identified as a suspect
[CLICK] At the end of this window, BreakHammer sees that the thread stayed benign and restores its memory bandwidth
[CLICK] Where in the last window, our thread continues to stay benign and uses its full memory bandwidth
=====
Have guides, rectangle without border can help
Bad whitespace usage
Check TCM, Atlas, BlockHammer again

## Slide 41: Outline
Background
Conclusion
BreakHammer
Evaluation
Motivation
Notes: I will continue with our evaluation of BreakHammer

## Slide 42: Evaluation Methodology
Performance and energy consumption evaluation using Ramulator 2.0 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
  Processor 4 cores, 4.2GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 64K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4
  Last-Level Cache 8 MiB (4-core)
Comparison Points: Integrated with 8 state-of-the-art RowHammer mitigations
Workloads: 4-core workload mixes from SPEC CPU2006/2017, TPC, MediaBench, YCSB  90 mixes with one attacker and  90 mixes with all benign
PARA [Kim+, ISCA 2014]
Graphene [Park+, MICRO 2020]
Hydra [Qureshi+, ISCA 2022]
TWiCe [Lee+, ISCA 2019]
AQUA [Saxena+, MICRO 2022]
REGA [Marazzi+, S&P 2023]
RFM [JEDEC 2020]
PRAC [JEDEC 2024]
Notes: We integrate BreakHammer with 8 state-of-the-art RowHammer mitigation mechanisms
And compare BreakHammer paired mechanisms against baseline solutions without BreakHammer
[CLICK] We evaluate a wide range of applications chosen from five major benchmark suites and create two type of workload mixes
[CLICK] We create 90 mixes where one core is mounting a memory performance attack by triggering many RowHammer-preventive actions
[CLICK] And 90 mixes where all applications are benign

## Slide 43: Evaluation Results
1)
Under Attack
2)
No Attack
Notes: Lets start by discussing systems [CLICK] that are under attack

## Slide 44: Evaluation Results
1)
Under Attack
2)
No Attack
Notes: Lets start by discussing systems [CLICK] that are under attack

## Slide 45: Preventive Action Count and Its Scaling
Lower is worse
Higher is worse
No BreakHammer
With
BreakHammer
~34x
Notes: We first take a look at BreakHammer’s impact on the number of RowHammer preventive actions performed
[CLICK] Here, the X axis is the decreasing RowHammer threshold
[CLICK] the Y axis is the preventive action count normalized to the preventive count of the system without BreakHammer at a threshold of 4K
[CLICK] the blue line shows the system without BreakHammer
[CLICK] and the orange line shows the system with BreakHammer
[CLICK] As an example, this point on the figure depicts that PRAC performs approximately 30 times more preventive actions when the RowHammer threshold decreases from 4K to 128
[CLICK] and when PRAC is paired with BreakHammer at the same threshold, we observe 80% reduction in the number of preventive actions performed
[CLICK] When we look at all of our results
====
More than 30x
Approximately 34x
Just say significantly maybe

## Slide 46: Preventive Action Count and Its Scaling
Lower is worse
Higher is worse
No BreakHammer
With
BreakHammer
~80% reduction
with BreakHammer
Notes: We first take a look at BreakHammer’s impact on the number of RowHammer preventive actions performed
[CLICK] Here, the X axis is the decreasing RowHammer threshold
[CLICK] the Y axis is the preventive action count normalized to the preventive count of the mechanism without BreakHammer at a threshold of 4K
[CLICK] the blue line shows the system without BreakHammer
[CLICK] and the orange line shows the system with BreakHammer
[CLICK] As an example, this point on the figure depicts that PRAC performs approximately 30 times more preventive actions when the RowHammer threshold decreases from 4K to 128
[CLICK] and when PRAC is paired with BreakHammer at the same threshold, we observe 80% reduction in the number of preventive actions performed
[CLICK] When we look at all of our results

## Slide 47: Preventive Action Count and Its Scaling
BreakHammer significantly reduces (72% on average) the number of preventive actions performed across all mechanisms
Notes: We observe that BreakHammer significantly reduces the number of preventive actions performed across all mechanisms and all thresholds

## Slide 48: Memory Latency Impact at NRH=64
Higher is worse
No BreakHammer
With
BreakHammer
No Defense
50% of requests are
served within 200ns
Notes: We continue by evaluating BreakHammer’s effect on benign application memory latency at a RowHammer threshold of 64
[CLICK] the X axis is the memory latency percentiles
[CLICK] the Y axis is the memory latency of benign applications in nanoseconds
[CLICK] the blue line shows a system without BreakHammer
[CLICK] the orange line shows a system with BreakHammer
[CLICK] and the dashed dark line shows the system with no RowHammer defense
[CLICK] As an example, this point on the blue line means that 50% of all memory requests are served within 200ns
[CLICK] When we look at all of our results
====
Don’t mention the background color

## Slide 49: Memory Latency Impact at NRH=64
BreakHammer reduces memory latency across all mechanisms
Notes: We observe that BreakHammer reduces the memory latency of all evaluated RowHammer solutions across all percentile values

## Slide 50: Performance Impact and Its Scaling
BreakHammer significantly increases (81% on average) PRAC’s performance
Lower is worse
Higher is better
76%
61%
43%
87%
93%
98%
105%
Notes: We analyze effect of reduced RowHammer-preventive action count and improved memory access latency on system performance
[CLICK] Here, the X axis is the decreasing RowHammer threshold
[CLICK] the Y axis is the system performance of benign applications normalized to a system with no RowHammer defense
[CLICK] Blue bars identify mechanisms without BreakHammer and orange bars present mechanisms with BreakHammer
[CLICK] For PRAC, we see that BreakHammer significantly increases the performance

## Slide 51: Performance Impact and Its Scaling
BreakHammer significantly increases system performance (90% on average)
As RowHammer threshold decreases, RowHammer mitigation mechanisms incur increasing performance overhead
Notes: When we look at the trends on other evaluated RowHammer mitigation mechanisms we see that
[CLICK] as RowHammer thresholds decreases, all evaluated RowHammer mitigation mechanisms incur increasing performance overhead
[CLICK] and BreakHammer greatly increases system performance for all evaluated solution

## Slide 52: DRAM Energy Impact and Its Scaling
BreakHammer significantly reduces (by 55% on average) PRAC’s energy consumption
Lower is worse
Lower is better
43%
51%
55%
57%
58%
59%
60%
Notes: We also analyze BreakHammer’s impact on DRAM energy consumption
[CLICK] Here, the X axis is the decreasing RowHammer threshold
[CLICK] the Y axis is the DRAM energy consumption normalized to a system with no RowHammer defense
[CLICK] Bars identify mechanisms with and without BreakHammer
[CLICK] For PRAC, we see that BreakHammer significantly reduces the DRAM energy consumption

## Slide 53: DRAM Energy Impact and Its Scaling
BreakHammer significantly decreases energy consumption (by 55% on average)
As RowHammer threshold decreases, RowHammer mitigation mechanisms consume significantly increasing DRAM energy
Notes: When we look at the trends on other evaluated RowHammer mitigation mechanisms we see that
[CLICK] as RowHammer thresholds decreases, all evaluated RowHammer mitigation mechanisms consume increasingly more DRAM energy
[CLICK] and BreakHammer reduces DRAM energy consumption for all evaluated solution

## Slide 54: Under Attack Summary
BreakHammer significantly reduces the performance and energy overheads
of existing RowHammer mitigation mechanisms when a memory performance attack is present
BreakHammer accurately detects suspect threads
1)
BreakHammer effectively reduces
the memory interference caused by suspect threads
2)
Notes: To summarize
[CLICK] BreakHammer significantly reduces the negative performance and energy overheads of
existing RowHammer mitigation mechanisms when a memory performance attack is present
[CLICK] These benefits are because BreakHammer accurately detects suspect threads
[CLICK] and effectively reduces the memory interference caused by suspect threads

## Slide 55: Evaluation Results
1)
Under Attack
2)
No Attack
Notes: Lets start by discussing systems [CLICK] that are under attack

## Slide 56: No Attack Summary
Across 90 four-core benign workload mixes:
BreakHammer slightly (<1%) improves
  memory access latency
  system performance
  DRAM energy efficiency
Notes: Across 90 four-core benign workload mixes
Even though it is not our goal to improve the performance of benign systems
We observe that BreakHammer slightly improves
[CLICK] memory access latency
[CLICK] system performance
[CLICK] DRAM energy efficiency

## Slide 57: More in the Paper
More implementation details
  Resetting BreakHammer counters
  Tracking software threads
  Throttling DMA and systems without caches
  Configuration parameters
Security analysis
  Upper bound on the overhead an attacker can cause
  Security against multi-threaded attackers
Performance evaluation
  Unfairness results
  Sensitivity to memory intensity of workloads
  Comparison to BlockHammer
  Sensitivity analysis of BreakHammer parameters
Notes: I would like to also refer you to our paper for more details on:
BreakHammer’s implementation, such as resetting counters or tracking software threads
[CLICK] Our security analysis, where we present an upper bound for attacker activity
and discuss multi-threaded attackers that try to defeat BreakHammer
[CLICK] Also more evaluations on unfairness and sensitivity to memory intensity
With detailed results on all benign workloads and more
=====
Backup for BlockHammer and BLISS, maybe say throttling here

## Slide 58: The Paper
https://arxiv.org/abs/2404.13477
Notes: Our paper is available on arXiv, accessible through this link or QR code

## Slide 59: Outline
Background
Conclusion
BreakHammer
Evaluation
Motivation
Notes: Now I will conclude my talk

## Slide 60: Conclusion
Key Results:
Under attack:
  Significantly improves system performance (by 90% on average)
  Significantly reduces energy consumption (by 55% on average)
No attack:
  Slightly (<1%) improves performance and energy consumption
Key Mechanism: BreakHammer
Observes triggered RowHammer-preventive actions
Identifies threads that trigger many preventive actions (i.e., suspect threads)
Reduces the memory bandwidth usage of the suspect threads
https://github.com/CMU-SAFARI/BreakHammer
Key Exploit: Mount a memory performance attack by triggering RowHammer-preventive actions to block memory accesses for long periods of time
Notes: We introduce the idea that it is possible to mount a memory performance attack by…
[CLICK] We propose BreakHammer: which
Observes triggered RowHammer-preventive actions
Identifies threads that trigger many of these actions
And reduces the memory bandwidth usage of suspect threads
[CLICK] Our evaluations show that:
When an attacker is present, BreakHammer accurately throttles the attacker which significantly improves performance and reduces energy
And when all applications are benign, BreakHammer slightly improves performance and reduces energy consumption

## Slide 61: Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/BreakHammer
Notes: Our BreakHammer implementation and all datasets are fully open-sourced and artifact evaluated

## Slide 62: BreakHammer: Enhancing RowHammer Mitigations by Carefully Throttling Suspect Threads
Oğuzhan Canpolat A. Giray Yağlıkçı Ataberk Olgun İsmail E. Yüksel
Yahya C. Tuğrul Konstantinos Kanellopoulos Oğuz Ergin Onur Mutlu
Venue : MICRO 2024
Presenter : A. Giray Yaglikci
Date : 27 April 2026
Notes: Hi all. I am Oğuzhan, very excited to be here and be able to present our work BreakHammer: Enhancing RowHammer Mitigations by Carefully Throttling Suspect Threads.

## Slide 63: Strengths
The paper tackles an important problem: Performance and energy overheads of RowHammer mitigation mechanisms
BreakHammer is a lightweight and effective mechanism
BreakHammer can be integrated with many existing RowHammer mitigations
The authors already explain and open source integration with 8 mitigations
Evaluation shows that BreakHammer
  alleviates the negative impact of a RowHammer attack on system performance and energy consumption
  does not slowdown benign workloads
BreakHammer’s implementation and evaluation scripts are opensourced
…

## Slide 64: Weaknesses
The memory performance attack is not demonstrated on a real system
BreakHammer is a hardware-level mechanism
  Does not have the context of software threads, processes, users, and address spaces
  Cannot track an attacker across threads and processes
As a memory controller-based mechanism, BreakHammer cannot observe the internals of in-DRAM solutions
  A thread’s score can increase if it performs a few activations to each of many rows
  Processing in Memory (PiM) enables computation within DRAM chips
    PiM cores generate memory requests within DRAM chips (after BreakHammer)
    BreakHammer cannot identify RowHammer attacks performed from within PiM cores
Majority of the plots are bar plots, and they are not very easy to read
…

## Slide 65: Avoid Rat Hole Discussions
Source: https://www.cse.wustl.edu/~jain/iucee/ftp/k_10adp.pdf
Source: P. Jarupunphol, “Using Buddhist Insights to Analyse the Cause of System Project Failures,” Ph.D. Thesis, 2013

## Slide 66: Every work has strengths and weaknesses
Papers are filtered into our class as they have merit
They should already emphasize their strengths: start with their major contributions
There is always room for improvement, so there are weaknesses
Some papers acknowledge some of their weaknesses
Many weaknesses are not obvious, but you have a brain and many others’ brains
Check the arguments in papers that improve the paper you present
Important! You should be skeptical about those claims too. Practice caution!
Jeonghyun Woo and Prashant J. Nair, "Dapper: A Performance-Attack-Resilient Tracker for RowHammer Defense," in HPCA, 2025.

## Slide 67: Discussion Points
Some bad discussion point examples for this paper:
  RowHammer is a problem for DRAM. What about other memory technologies?  This is a discussion way out of this paper’s scope
  What are the mitigation mechanisms integrated with BreakHammer?  Discussion is not a quiz for the audience, the goal is to brainstorm
  RowHammer mitigation mechanisms incur higher performance overheads with increasing DRAM density. Should we stop scaling DRAM density?  Too philosophical and arguably backwards looking
Weaknesses are your friends to find good discussion points
Find fundamental weaknesses
Ask: Can we do better?
Discuss how to do better

## Slide 68: Discussion Points
Example weakness: “Memory performance attacks are not demonstrated on a real system.”
Discussion point: Should we do that?
  A good starting point, but needs more work
  What is the benefit of demonstrating them? What research problem does it solve?
  Any papers solving that problem? What is missing?
  What is your solution?
    any hypothesis?
    key insights, observations, and ideas?
    expected results?
    What are some practical challenges?
      What do we need to reverse engineer?
      Do we have real systems that implement studied or other RowHammer mitigations?
Leading a discussion is more than throwing open-ended questions
Be constructive: how can we advance the state-of-the-art?

## Slide 69: Discussion Points
Example Weakness: “BreakHammer cannot track an attacker across threads and processes.”
Is this a problem? Yes. You can bypass BreakHammer via multithreading. Still no bitflips, but you can block memory
  Each thread activates a row a few times
  Cumulative activation count across threads triggers RowHammer mitigations
  RowHammer mitigations cause performance degradation and increase energy consumption
  Practically: BreakHammer becomes useless
Goal: Enable tracking RowHammer-based memory performance attacks across threads
Key idea: Hardware-OS cooperation
  BreakHammer collects scores at the hardware thread level
  OS sums up the scores of a process or user an identifies process- and user-level behavioral patterns
  OS performs throttling:
    OS asks BreakHammer to throttle memory accesses of a hardware thread
    OS deprioritizes suspicious users and processes in CPU scheduling
    OS uses memory bandwidth allocation features of modern processors
Any similar works?
  Fiedler et al., “Memory Band-Aid: A Principled RowHammer Defense-in-Depth,” in NDSS, 2026.
  This is a software-only throttling-based RowHammer mitigation mechanism, aiming to prevent bitflips
  As a software-level mechanism, it can incur very high performance overheads, opposite of what we want
Expected results:
  Providing an end-to-end solution to RowHammer, where
  bitflips are prevented within the DRAM chip
  attackers are stopped at the OS level

## Slide 70: Computer Architecture Seminar/Proseminar Lecture 1b: Example Presentation
A. Giray Yaglikci
27 April 2026